Diana Kanecki, DM(ABD), MBA, ACS, Bio. Sci.

K-EDGE 1 Project

An edge computing hardware project to use off the shelf (OSF) and Arduino Open Source Components (AOSC) for developing a 2048 K-Edge-1 supercomputer for control, Intelligent Thinking Systems, AI, MI, Aerospace, and IOT (internet of things systems) from small to huge. The ideas include distributed processing with a flexible path control from a master module and allowing node modules to switch roles as master or node.

Introduction

KNODE 20 – MASTER DEV (PASSED)

SOURCE CODE

Source Code

1. // ***********************************************************************
2. // KNODE 2-0 . November 11, 2022
3. // Added masterStar via register=3
4. // Needed to test
5. // **********************************************************************
6. // KNODE 2.0 - August 26, 2022
7. // readRegister and writeRegister works!
8. // ***********************************************************************
9. // Sept 29, 2022 - r18
10. // Dual register problem solved
11. // Solution - each register needs its' own clockPin and latchPin lines
12. // - using latchPinCSR and clockPin2 for register 0
13. // - using latchPin and clockPin for register 1
14. // Sept 27, 2022 - r18
15. // new masking works (nodeID<<4)+ (regID)
16. // but only correct read of register 1 in Node 0 state, all other states gives incorrect value
17. // Sept 23, 2022 - r17
18. // initial round robin test
19. // round robit for mux node selects works, but readRegister1() has value error in loop test
20. // cross talk between reg0 and reg1 due to *OE (active low) control [gnd vd *S0]
21. // --- idea to use d0/other pin for output enable (OE) control rather than mux
22. // --- or use 8255 peripheral chip
23. // --- cant have two or more *OE's active at a time, only 1
24. // --- need to control which register *OE is active at a time
25. // --- for round robin to read proper register
26. //
27. // round robin works for node selection with mux (*OE register control needs addition)
28. // ***********************************************************************
29. // Sept 19, 2022 - r16
30. // Using AdaFruit display monitor within interrupt
31. // Prep for round-robin master/slave test
32. // loop and data xfer tests works.
33. // Sept 13, 2022- r15
34. // ISR routine works and gets proper value from setup of register 1
35. // (need to think of using intell 8255 for easier peripheral control rather homebrew method being used)
36. // add link to mux *S0, *S1(reg1), *S2(reg2), etc for multiple register control past reg 1
37. // dual D4 link from two processors work
38. // -----------------------------------------------------------------------
39. // to write register 1
40. // use:
41. // writeRegister0(1);
42. // writeRegister1(data);
43. // -----------------------------------------------------------------------
44. // to read register 1
45. // use:
46. // value=readRegister1();
47. // Note --- if writeRegister0(1) is used will read wrong value
48. // --- glitch still exists
49. // ***********************************************************************
50. // Sept 10, 2022- r12
51. // Added bus control, D0, which checks is bus is availble, D0=1, or busy, D0=0
52. // works with testModule5()
53. // Added invalid register access error message as default: statement
54. // Added "-r12" terminator in screen msgs so to know which version of Master code is running
55. // ***********************************************************************
56. // Sept 6, 2022 - r11
57. // Need 74157 for 1 to 4 selector for CLK pin to avoid activating all pins for more than 1 register
58. // work around is using D4 on second CLK pin
59. // Sept 6, 2022 - r9
60. // Update for 4 latch registers and shared CLK, Din, Dout
61. //
62. // *****************************************************************
63. // * Multi Bus Setup Constants
64. // ****************************************************************
65. //
66. // Absolute pin setup as D3 is for use with esp8266 (NODE 1.0-12E)
67. //int latchPin = D3; // Reg1 --- gpio 0 pin 11 on 74595 chip, registers 1-3
68. //int latchPinCSR = D4; // Reg0 --- gpio 2 pin 11 on register 0
69. //int latchPinReg2= 16; // Reg2 --- gpio 16, D0 on esp8266
70. //int latchPinReg3= 10; // Reg3 --- gpio 10, SD3 on esp8266
71. //
72. //int clockPin = D5; // gpio 14 pin 12 on 74595 chip
73. //int dataPinOut = D7; // gpio 13 pin 14 on 74595 chip;
74. //int dataPinIn = D6; // gpio 12 pin 9 on 74595 chip
75. // int interruptPin= D8; // gpio 15
76. //
77. // int clearBus = 0;
78. // *** END Multi Bus Setup Constants ***
79. // ************************************************************
80. // Sept 3, 2022
81. // Revision 8
82. // Code for readRegister1 works, need to use MUX *S0 attached to OE* (pin 13
83. // to control output
84. // *S0 means *S0 is active low
85. // ***********************************************************************
86. // Sept 1, 2022
87. // Second MUX works. I/O routines work with proper formatting
88. // ***********************************************************************
89. // August 31 --- Version R7
90. // CSR (Control Status Register) work properly with 74138 decoders for register selection
91. // --- next test: read/write from registers 1 to 4
92. //
93. // ***********************************************************************
94. // August 24, 2022
95. // Master Mode of SPI-1-R4
96. // =======================================================================
97. // August 22, 2022
98. // SPI-1-r3 with OLED 128x64, device ID using shift registe 74HC595, and SPI
99. // Multiple Bus Class Use
100. // (C) 2022 Diana Kanecki, All Rights Reserved
101. // Diana Kanecki, DM(ABD), MBA, ACS, Bio. Sci.
102. //
103. // **********************************************************************
105. /**************************************************************************
106. This is an example for our Monochrome OLEDs based on SSD1306 drivers
108. Pick one up today in the adafruit shop!
109. ------> http://www.adafruit.com/category/63_98
111. This example is for a 128x32 pixel display using I2C to communicate
112. 3 pins are required to interface (two I2C and one reset).
114. Adafruit invests time and resources providing this open
115. source code, please support Adafruit and open-source
116. hardware by purchasing products from Adafruit!
118. Written by Limor Fried/Ladyada for Adafruit Industries,
119. with contributions from the open source community.
120. BSD license, check license.txt for more information
121. All text above, and the splash screen below must be
122. included in any redistribution.
123. **************************************************************************/
125. //#include <SPI.h>
126. #include <Wire.h>
127. #include <Adafruit_GFX.h>
128. #include <Adafruit_SSD1306.h>
130. #define SCREEN_WIDTH 128 // OLED display width, in pixels
131. //#define SCREEN_HEIGHT 32 // OLED display height, in pixels
132. #define SCREEN_HEIGHT 64 // OLED display height, in pixels (determines character height - changable for better reading)
134. // Declaration for an SSD1306 display connected to I2C (SDA, SCL pins)
135. // The pins for I2C are defined by the Wire-library.
136. // On an arduino UNO: A4(SDA), A5(SCL)
137. // On an arduino MEGA 2560: 20(SDA), 21(SCL)
138. // On an arduino LEONARDO: 2(SDA), 3(SCL), ...
139. #define OLED_RESET -1 // Reset pin # (or -1 if sharing Arduino reset pin)
140. //#define SCREEN_ADDRESS 0x3C ///< See datasheet for Address; 0x3D for 128x64, 0x3C for 128x32
141. #define SCREEN_ADDRESS 0x3C
142. Adafruit_SSD1306 display(SCREEN_WIDTH, SCREEN_HEIGHT, &Wire, OLED_RESET);
144. #define NUMFLAKES 10 // Number of snowflakes in the animation example
146. #define LOGO_HEIGHT 16
147. #define LOGO_WIDTH 16
148. static const unsigned char PROGMEM logo_bmp[] =
149. { 0b00000000, 0b11000000,
150. 0b00000001, 0b11000000,
151. 0b00000001, 0b11000000,
152. 0b00000011, 0b11100000,
153. 0b11110011, 0b11100000,
154. 0b11111110, 0b11111000,
155. 0b01111110, 0b11111111,
156. 0b00110011, 0b10011111,
157. 0b00011111, 0b11111100,
158. 0b00001101, 0b01110000,
159. 0b00011011, 0b10100000,
160. 0b00111111, 0b11100000,
161. 0b00111111, 0b11110000,
162. 0b01111100, 0b11110000,
163. 0b01110000, 0b01110000,
164. 0b00000000, 0b00110000 };
166. // *****************************************************************
167. // * Multi Bus Setup Constants
168. // ****************************************************************
170. // Absolute pin setup as D3 is for use with esp8266 (NODE 1.0-12E)
171. int latchPin = D3; // Reg1 --- gpio 0 pin 11 on 74595 chip, registers 1-3
172. int latchPinCSR = D4; // Reg0 --- gpio 2 pin 11 on register 0
173. //int latchPinReg2= 16; // Reg2 --- gpio 16, D0 on esp8266
174. //int latchPinReg3= 10; // Reg3 --- gpio 10, SD3 on esp8266
175. //
176. int busPin = D0;
177. int clockPin = D5; // gpio 14 pin 12 on 74595 chip
178. //int clockPin2 = 10; // pin12 on 74595 chip
179. int dataPinIn = D6; // gpio 12 pin 9 on 74595 chip
180. int dataPinOut = D7; // gpio 13 pin 14 on 74595 chip;
181. int interruptPin= D8; // gpio 15
182. int slaveLatch = D8;
183. int clockPin2 = D9; // 10; // sd3
185. //
186. int clearBus = 0;
187. int maxRegisters = 1;
188. int OEReg1 = 10; // OK - added 9/22/2022 sd3
190. // *** END Multi Bus Setup Constants ***
192. volatile int j=0;
193. volatile int NodeId=0;
194. char buff[100]= "Hello from Host\n\0";
195. volatile int index1;
196. volatile bool receivedone;
197. volatile bool masterStart;
198. //int int1 = D8; //
200. int lastValue1 = 0;
201. int lineCount1 = 0;
202. int nullRegister = 3;
204. unsigned long button_time = 0;
205. unsigned long last_button_time = 0;
206. int y = 0;
207. bool ledToggle = false;
208. int intValueRd=0;
210. void testMode() {
211. /*
212. testdrawline(); // Draw many lines
214. testdrawrect(); // Draw rectangles (outlines)
216. testfillrect(); // Draw rectangles (filled)
218. testdrawcircle(); // Draw circles (outlines)
220. testfillcircle(); // Draw circles (filled)
222. testdrawroundrect(); // Draw rounded rectangles (outlines)
224. testfillroundrect(); // Draw rounded rectangles (filled)
226. testdrawtriangle(); // Draw triangles (outlines)
228. testfilltriangle(); // Draw triangles (filled)
230. testdrawchar(); // Draw characters of the default font
232. testdrawstyles(); // Draw 'stylized' characters
234. testscrolltext(); // Draw scrolling text
236. testdrawbitmap(); // Draw a small bitmap image
238. // Invert and restore display, pausing in-between
239. display.invertDisplay(true);
240. delay(1000);
241. display.invertDisplay(false);
242. delay(1000);
244. testanimate(logo_bmp, LOGO_WIDTH, LOGO_HEIGHT); // Animate bitmaps
245. */
247. }
249. void setup() {
250. Serial.begin(9600);
251. pinMode(latchPin,OUTPUT);
252. pinMode(clockPin,OUTPUT);
253. //pinMode(clockPin2,OUTPUT);
254. pinMode(latchPinCSR,OUTPUT);
255. //pinMode(latchPinReg2,OUTPUT);
257. //pinMode(latchPinReg3,OUTPUT);
258. pinMode(dataPinOut,OUTPUT);
259. pinMode(clockPin2,OUTPUT);
260. digitalWrite(clockPin2,LOW);
261. pinMode(dataPinIn,INPUT);
263. pinMode(busPin,OUTPUT);
264. digitalWrite(busPin,LOW);
265. pinMode(busPin,LOW);
267. // *******************************************************************************
268. // *** Multibus setup code - quietBus()
269. // *******************************************************************************
270. digitalWrite(latchPin,LOW);
271. shiftOut(dataPinOut,clockPin, MSBFIRST,clearBus); // clear bus
272. digitalWrite(latchPin,HIGH);
274. //digitalWrite(latchPinReg2,HIGH);
275. //digitalWrite(latchPinReg3,HIGH);
276. // *** END Multibus setup code ***************************************************
279. // SSD1306_SWITCHCAPVCC = generate display voltage from 3.3V internally
280. if(!display.begin(SSD1306_SWITCHCAPVCC, SCREEN_ADDRESS)) {
281. Serial.println(F("SSD1306 allocation failed"));
282. for(;;); // Don't proceed, loop forever
283. }
285. // Show initial display buffer contents on the screen --
286. // the library initializes this with an Adafruit splash screen.
287. display.display();
288. delay(2000); // Pause for 2 seconds
290. // Clear the buffer
291. display.clearDisplay();
293. // Draw a single pixel in white
294. display.drawPixel(10, 10, SSD1306_WHITE);
296. // Show the display buffer on the screen. You MUST call display() after
297. // drawing commands to make them visible on screen!
298. display.display();
299. delay(2000);
300. // display.display() is NOT necessary after every single drawing command,
301. // unless that's what you want...rather, you can batch up a bunch of
302. // drawing operations and then update the screen all at once by calling
303. // display.display(). These examples demonstrate both approaches...
305. // testMode();
307. // ************************************************************
308. // *** Multibus Setup Codes
309. // ************************************************************
311. index1=0;
312. receivedone=false;
313. masterStart = true;
315. // Start at top-left corner
316. display.clearDisplay();
318. display.setTextSize(1); // Normal 1:1 pixel scale
319. display.setTextColor(SSD1306_WHITE); // Draw white text
320. display.setCursor(0,0);
321. lineCount1=0;
323. pinMode(15,INPUT_PULLUP);
324. // use GPIO 15 -> D8
325. attachInterrupt(digitalPinToInterrupt(D8),testInt8,CHANGE);
327. writeRegister0(1);
328. writeRegister1(5);
329. //delay(1000);
330. writeRegister0(0);
331. }
333. ICACHE_RAM_ATTR void testInt8(){
335. int value = 0;
336. noInterrupts();
337. button_time = millis();
338. //check to see if increment() was called in the last 250 milliseconds
339. if (button_time - last_button_time > 250){
340. // writeRegister0(1); // added 9/23/2022 to select reg1
341. value = readRegister1();
342. ledToggle = true;
343. intValueRd = value;
344. Serial.print("In Interupt r16- ");
345. Serial.print(" value retrieved is ");
346. Serial.println(value);
347. Serial.println();
348. // writeRegister1(value); added 9/23/2022
349. last_button_time = button_time;
351. }
352. interrupts();
353. }
355. void loop() {
356. Serial.print("in Host - r20 - ");
357. Serial.println(j);
358. lineCount1=0;
359. display.clearDisplay();
360. display.setCursor(0,0);
361. display.display();
363. writeStr1("Hello,fr Host! r20 ");
364. writeInt1(j);
365. writeLn1();
366. delay(1000);
368. if (masterStart){
369. masterStart=false;
370. writeStr1("...Init ND Rst");
371. writeLn1();
372. writeRegister0(3); // initate restart pulse
373. delay(2000);
374. writeRegister0(1); // stop restart pulse
375. }
377. writeStr1("...Contact Nd ");
378. writeInt1((j%4));
379. int m = (((j%4))<<4)+1;
380. writeStr1(" ");
381. writeInt1(m);
382. writeRegister0(m);
383. writeLn1();
384. delay(1000);
385. j++;
386. NodeId= NodeId++;
388. }
390. // **************************************************
391. // *** Register Routines
392. // **************************************************
393. void writeRegister0(int dataOut)
394. {
395. // Aug 31, 2022 - verified to work for register 0
396. // for use with any SIPO register as 74595 and 74165
398. //digitalWrite(latchPin,LOW); // OK - added 9/23/2022 to deselect reg1
399. digitalWrite(latchPinCSR,LOW);
400. shiftOut(dataPinOut,clockPin2, MSBFIRST,dataOut);
401. digitalWrite(latchPinCSR,HIGH);
402. //digitalWrite(latchPin,HIGH);
404. }
406. void writeRegister1(int dataOut)
407. {
408. // verified - Sept 3, 2022 - to work with 74595 chip
409. // Serial.println("... in writeRegister1()");
411. digitalWrite(latchPinCSR,LOW);
413. // works Sept 3, 2022
414. digitalWrite(latchPin,LOW);
415. shiftOut(dataPinOut,clockPin, MSBFIRST,dataOut);
416. digitalWrite(latchPin,HIGH);
418. digitalWrite(latchPinCSR,HIGH);
420. }
422. /*
423. void writeRegister2(int dataOut)
424. {
425. // Sept 6, 2022 --- Need to test
426. // Serial.println("... in writeRegister2()");
428. // works Sept 3, 2022
429. digitalWrite(latchPinReg2,LOW);
430. shiftOut(dataPinOut,clockPin, MSBFIRST,dataOut);
431. digitalWrite(latchPinReg2,HIGH);
432. }
434. void writeRegister3(int dataOut)
435. {
436. // Sept 6, 2022 --- need to test
437. // Serial.println("... in writeRegister2()");
439. // works Sept 3, 2022
440. digitalWrite(latchPinReg3,LOW);
441. shiftOut(dataPinOut,clockPin, MSBFIRST,dataOut);
442. digitalWrite(latchPinReg3,HIGH);
443. }
444. */
446. void writeCtrlRegToBus(int dataOut)
447. {
448. //digitalWrite(busPin,LOW);
449. writeRegister0(dataOut);
450. //digitalWrite(busPin,HIGH);
451. }
453. int readRegister0()
454. {
455. // Aug 31, 2022 - verified to work for register 0
456. // for special use with 74595 shift register SIPO
457. int value = 0;
458. int bitOrder = MSBFIRST;
460. digitalWrite(latchPin,LOW); // OK -added 9/23/2022 to block access to reg 0 while rd reg 1
462. for (int i = 0; i < 8; ++i) {
463. if (bitOrder == LSBFIRST)
464. value |= digitalRead(dataPinIn) << i;
465. else
466. value |= digitalRead(dataPinIn) << (7 - i);
467. digitalWrite(clockPin2, HIGH);
468. digitalWrite(clockPin2, LOW);
469. }
470. digitalWrite(latchPin,HIGH);
471. return(value);
472. }
474. int readRegister1()
475. {
476. // Sept 6, 2022 --- need to test
477. // need decoder for more than one register 74153
478. // because clk pin activates all at same time
480. int value = 0;
481. int bitOrder = MSBFIRST;
483. //Serial.println(" ... in readRegister1()");
485. digitalWrite(latchPinCSR,LOW); // OK-added 9/23/2022 block reading register 0
487. for (int i = 0; i < 8; ++i) {
488. if (bitOrder == LSBFIRST)
489. value |= digitalRead(dataPinIn) << i;
490. else
491. value |= digitalRead(dataPinIn) << (7 - i);
493. digitalWrite(latchPin,LOW);
494. digitalWrite(clockPin, HIGH);
495. digitalWrite(clockPin, LOW);
496. digitalWrite(latchPin,HIGH);
497. }
499. writeRegister1(value); // added 9/27/2022
500. digitalWrite(latchPinCSR,HIGH);
501. return(value);
502. }
504. int readRegister2()
505. {
506. // Sept 6, 2022 --- Need to test
507. // need decoder for more than one register 74153
508. // because clk pin activates all at same time
509. int value = 0;
510. int bitOrder = MSBFIRST;
512. //Serial.println(" ... in readRegister2()");
514. if (2 <= maxRegisters)
515. {
517. for (int i = 0; i < 8; ++i) {
518. if (bitOrder == LSBFIRST)
519. value |= digitalRead(dataPinIn) << i;
520. else
521. value |= digitalRead(dataPinIn) << (7 - i);
523. digitalWrite(clockPin, HIGH);
524. digitalWrite(clockPin, LOW);
525. }
526. }
527. else value=0;
529. return(value);
530. }
532. int readRegister3()
533. {
534. // Sept 6, 2022 --- Need to test
535. // need decoder for more than one register 74153
536. // because clk pin activates all at same time
537. int value = 0;
538. int bitOrder = MSBFIRST;
540. if (3 <= maxRegisters)
541. {
542. for (int i = 0; i < 8; ++i) {
543. if (bitOrder == LSBFIRST)
544. value |= digitalRead(dataPinIn) << i;
545. else
546. value |= digitalRead(dataPinIn) << (7 - i);
548. //digitalWrite(latchPinReg3,LOW);
549. digitalWrite(clockPin, HIGH);
550. digitalWrite(clockPin, LOW);
551. //digitalWrite(latchPinReg3,HIGH);
552. }
553. }
554. else value=0;
555. return(value);
556. }
558. // *****************************************************
559. // *** I/O Routines
560. // *****************************************************
561. void writeInt1( int val){
562. // Sept 1, 2022 - verified to work with formatting
563. display.print(val);
564. display.display();
565. }
567. void writeStr1( char str1[]){
568. // Sept 1, 2022 - verified to work with formatting
569. display.print(str1);
570. display.display();
571. }
573. void writeLnStr1( char str1[]){
574. // Sept 1, 2022 - verified to work with formatting
575. display.println(str1);
576. display.display();
577. lineCount1++;
578. if (lineCount1 > 6)
579. {
580. delay(2000);
581. display.clearDisplay();
582. display.setCursor(0,0);
583. display.display();
584. lineCount1=0;
585. }
586. display.clearDisplay();
587. display.display();
588. }
590. void writeLn1() {
591. // Sept 1, 2022 - verified to work with formatting
592. display.println();
593. display.display();
594. lineCount1++;
595. if (lineCount1 > 6)
596. {
597. delay(2000);
598. display.clearDisplay();
599. display.setCursor(0,0);
600. display.display();
601. lineCount1=0;
602. }
603. }
605. // ****************************************************************
606. // *** Test Routines
607. // ****************************************************************
608. void testModule6(){
610. //writeRegister0(1);
611. writeRegister1(5);
612. delay(1000);
614. // for (int i=0; i<4; i++){
615. writeRegister0(((j%4)<<4)+1);
616. //delay(500);
617. if (ledToggle)
618. {
619. display.clearDisplay();
620. display.setCursor(0,0);
621. display.display();
622. writeStr1("Process Int r18 ");
623. writeLn1();
624. writeStr1("Value read->");
625. writeInt1(intValueRd);
626. writeLn1();
627. display.display();
628. ledToggle=false;
629. delay(2000);
630. };
631. // }
632. // delay(1000);
633. int value2 = readRegister1();
634. writeStr1("Value read->");
635. writeInt1(value2);
636. writeLn1();
637. display.display();
638. delay(1000);
640. }
642. void testModule1()
643. {
644. // verified to work Aug 28, 2022
645. /*
646. for(int k=0; ((k < sizeof buff) && (buff[k]!=0)); k++ ){
647. Serial.print("Sending char(");
648. Serial.print((char)buff[k]);
649. Serial.println(")");
650. display.setCursor(0,20); // Start at top-left corner
651. display.print(F("Sending ch ("));
652. display.print(buff[k]);
653. display.print(") ");
654. display.println(k);
655. display.display();
657. digitalWrite(slaveLatch,LOW); // slave select ON
658. digitalWrite(slaveLatch,HIGH); // slave select OFF
659. delay(1000);
660. }
661. */
662. /*
663. display.setTextColor(SSD1306_WHITE); // Draw white text
664. display.setCursor(0,20); // Start at top-left corner
665. display.print(buff);
666. display.print(j);
667. display.println();
668. display.display();
669. */
670. /*
671. if (receivedone)
672. {
673. buff[index1]= 0;
674. display.setTextSize(1); // Normal 1:1 pixel scale
675. display.setTextColor(SSD1306_WHITE); // Draw white text
676. display.setCursor(3,0); // Start at top-left corner
677. display.print(F("Msg from Host! "));
678. display.print(buff);
679. display.println();
680. display.display();
682. index1=0;
683. receivedone=false;
684. }
685. */
686. // *************************************************************
687. // *** Device ID Register Code using 74HC595
688. // *************************************************************
690. // Device ID Register Control Code for Master Node
691. for (int i=0; i<256; i++) {
692. //display.setCursor(0,20);
693. display.print("Writing ... ");
694. display.println(i);
695. //display.println();
696. display.display();
697. lineCount1++;
698. Serial.print("Writing ...");
699. Serial.println(i);
700. writeRegister0(i);
702. lastValue1 = readRegister0();
704. //display.setCursor(0,30);
705. display.print("Reading ... ");
706. display.print(lastValue1);
707. display.println();
708. display.display();
709. lineCount1++;
710. Serial.print("Reading LastValue =");
711. Serial.println(lastValue1);
712. Serial.print("LineCount1 is ");
713. Serial.println(lineCount1);
714. Serial.println("\n");
715. // if ((i % 4) == 0)
716. // if ((lineCount1 & 8) == 0) // display first two entries then clears
717. if (((lineCount1 % 8) == 0) || (lineCount1 > 8))
718. {
719. delay(1000);
720. display.clearDisplay();
721. display.setCursor(0,0);
722. display.display();
723. lineCount1=0;
724. }
725. delay(1000);
726. }
727. }
729. void testModule2()
730. {
731. // updated Sept 1, 2022 -- added test for mux in 8 to 12
732. int lastValue1;
734. writeStr1("IN testModule2() ");
735. writeLn1();
736. delay(1000);
737. for (int i=0; i<4;i++)
738. {
739. writeRegister0(i);
741. writeStr1("Writing ... ");
742. writeInt1(i);
743. //display.println();
744. writeLn1();
746. Serial.print("Writing ...");
747. Serial.print(i);
749. lastValue1 = readRegister0();
751. writeStr1("Reading ... ");
752. writeInt1(lastValue1);
753. //display.println();
754. writeLn1();
756. Serial.print(" Reading ...");
757. Serial.print(lastValue1);
758. Serial.print(" LineCount1 is ");
759. Serial.println(lineCount1);
760. Serial.println();
761. delay(1000);
762. }
763. /*
764. for (int i=8; i<12;i++)
765. {
766. writeRegister0(i);
768. writeStr1("Writing ... ");
769. writeInt1(i);
770. //display.println();
771. writeLn1();
773. Serial.print("Writing ...");
774. Serial.println(i);
775. Serial.print("LineCount1 is ");
776. Serial.println(lineCount1);
777. Serial.println("\n");
778. delay(1000);
779. }
780. */
781. }
783. void testModule3()
784. {
785. // sept 6, 2022 --- verified to work
786. // started Sept 3, 2022 -- added test for mux in 8 to 12
787. int lastValue=0;
789. writeStr1("IN testModule3() ");
790. writeLn1();
791. delay(1000);
792. for (int i=0; i<16;i++)
793. {
794. writeRegister0(1); // added Spet 13, 2022 -- cant work embedded in writeRegister0()
795. writeRegister1(i);
797. writeStr1("Writing ... ");
798. writeInt1(i);
799. //display.println();
800. writeLn1();
802. Serial.print("Writing ...");
803. Serial.println(i);
804. Serial.print("LineCount1 is ");
805. Serial.println(lineCount1);
806. Serial.println("\n");
807. lastValue1 = readRegister1();
809. Serial.print("Reading ...");
810. Serial.println(lastValue1);
811. Serial.println();
812. //display.setCursor(0,30);
813. writeStr1("Reading ... ");
814. writeInt1(lastValue1);
815. writeLn1();
816. display.display();
818. writeRegister1(i);
819. delay(1000);
820. }
821. }
823. void testModule5(int regNum)
824. {
826. // started Sept 3, 2022 -- added test for mux in 8 to 12
827. int lastValue=0;
828. int busStatus = 1;
830. writeStr1("IN testModule5()-r12 ");
831. writeLn1();
832. delay(1000);
834. busStatus=digitalRead(busPin);
835. while (busStatus !=0){
836. writeStr1(" ... Bus Busy, Waiting");
837. writeLn1();
838. delay(1000);
839. busStatus = digitalRead(busPin);
840. }
841. writeStr1(" ... Bus Ready");
842. writeLn1();
843. for (int i=0; i<16;i++)
844. {
845. switch(regNum){
846. case 0: writeRegister0(i);
847. break;
848. case 1:
849. writeRegister0(1);
850. writeRegister1(i);
851. break;
852. /*
853. case 2:
854. writeRegister0(2);
855. writeRegister2(i);
856. break;
857. case 3:
858. writeRegister0(3);
859. writeRegister3(i);
860. break;
861. */
862. default:
863. writeStr1(" ... INV reg ");
864. writeRegister0(regNum);
865. delay(1000);
866. writeInt1(regNum);
867. writeLn1();
868. break;
869. }
870. //writeRegister0(0);
871. //delay(1000);
873. writeStr1("Wr Reg ");
874. writeInt1(regNum);
875. writeStr1(" ->");
876. writeInt1(i);
877. //display.println();
878. writeLn1();
880. Serial.print("Writing Reg ");
881. Serial.print(regNum);
882. Serial.print("...");
883. Serial.print(i);
884. Serial.print(" LineCount1 is ");
885. Serial.print(lineCount1);
886. Serial.print(" Register->");
887. Serial.print(regNum);
888. switch(regNum){
889. case 0: lastValue1=readRegister0();
890. break;
891. case 1:
892. //writeRegister0(1);
893. lastValue1=readRegister1();
894. break;
895. /*
896. case 2: lastValue1=readRegister2();
897. break;
898. case 3: lastValue1=readRegister3();
899. break;
900. */
901. default:
902. writeStr1(" ... INV reg ");
903. writeRegister0(regNum);
904. delay(1000);
905. writeInt1(regNum);
906. writeLn1();
907. lastValue1 =0;
908. break;
909. }
910. //writeRegister0(0);
911. //delay(1000);
912. // lastValue1=readRegister1();
914. Serial.print(" Reading ...");
915. Serial.println(lastValue1);
916. Serial.println();
917. //display.setCursor(0,30);
918. writeStr1("Reading ... ");
919. writeInt1(lastValue1);
920. writeLn1();
921. display.display();
923. switch(regNum){
924. case 0: writeRegister0(i);
925. break;
926. case 1:
927. writeRegister0(1);
928. writeRegister1(i);
929. break;
930. /*
931. case 2: writeRegister2(i);
932. break;
933. case 3: writeRegister3(i);
934. break;
935. */
936. default:
937. writeStr1(" ... INV reg ");
938. writeRegister0(regNum);
939. delay(1000);
940. writeInt1(regNum);
941. writeLn1();
942. break;
943. }
944. //writeRegister0(0);
945. //delay(1000);
946. }
947. }
949. /*
950. void testModule4()
951. {
952. // Sept6, 2022 --- test module 4 verified to work
954. Serial.println("Hello from testModule4()");
955. digitalWrite(latchPinReg2,HIGH);
956. digitalWrite(latchPinReg3,LOW);
957. delay(1000);
958. digitalWrite(latchPinReg2,LOW);
959. digitalWrite(latchPinReg3,HIGH);
960. delay(1000);
961. }
963. */
965. void testdrawline() {
966. int16_t i;
968. display.clearDisplay(); // Clear display buffer
970. for(i=0; i<display.width(); i+=4) {
971. display.drawLine(0, 0, i, display.height()-1, SSD1306_WHITE);
972. display.display(); // Update screen with each newly-drawn line
973. delay(1);
974. }
975. for(i=0; i<display.height(); i+=4) {
976. display.drawLine(0, 0, display.width()-1, i, SSD1306_WHITE);
977. display.display();
978. delay(1);
979. }
980. delay(250);
982. display.clearDisplay();
984. for(i=0; i<display.width(); i+=4) {
985. display.drawLine(0, display.height()-1, i, 0, SSD1306_WHITE);
986. display.display();
987. delay(1);
988. }
989. for(i=display.height()-1; i>=0; i-=4) {
990. display.drawLine(0, display.height()-1, display.width()-1, i, SSD1306_WHITE);
991. display.display();
992. delay(1);
993. }
994. delay(250);
996. display.clearDisplay();
998. for(i=display.width()-1; i>=0; i-=4) {
999. display.drawLine(display.width()-1, display.height()-1, i, 0, SSD1306_WHITE);
1000. display.display();
1001. delay(1);
1002. }
1003. for(i=display.height()-1; i>=0; i-=4) {
1004. display.drawLine(display.width()-1, display.height()-1, 0, i, SSD1306_WHITE);
1005. display.display();
1006. delay(1);
1007. }
1008. delay(250);
1010. display.clearDisplay();
1012. for(i=0; i<display.height(); i+=4) {
1013. display.drawLine(display.width()-1, 0, 0, i, SSD1306_WHITE);
1014. display.display();
1015. delay(1);
1016. }
1017. for(i=0; i<display.width(); i+=4) {
1018. display.drawLine(display.width()-1, 0, i, display.height()-1, SSD1306_WHITE);
1019. display.display();
1020. delay(1);
1021. }
1023. delay(2000); // Pause for 2 seconds
1024. }
1026. void testdrawrect(void) {
1027. display.clearDisplay();
1029. for(int16_t i=0; i<display.height()/2; i+=2) {
1030. display.drawRect(i, i, display.width()-2*i, display.height()-2*i, SSD1306_WHITE);
1031. display.display(); // Update screen with each newly-drawn rectangle
1032. delay(1);
1033. }
1035. delay(2000);
1036. }
1038. void testfillrect(void) {
1039. display.clearDisplay();
1041. for(int16_t i=0; i<display.height()/2; i+=3) {
1042. // The INVERSE color is used so rectangles alternate white/black
1043. display.fillRect(i, i, display.width()-i*2, display.height()-i*2, SSD1306_INVERSE);
1044. display.display(); // Update screen with each newly-drawn rectangle
1045. delay(1);
1046. }
1048. delay(2000);
1049. }
1051. void testdrawcircle(void) {
1052. display.clearDisplay();
1054. for(int16_t i=0; i<max(display.width(),display.height())/2; i+=2) {
1055. display.drawCircle(display.width()/2, display.height()/2, i, SSD1306_WHITE);
1056. display.display();
1057. delay(1);
1058. }
1060. delay(2000);
1061. }
1063. void testfillcircle(void) {
1064. display.clearDisplay();
1066. for(int16_t i=max(display.width(),display.height())/2; i>0; i-=3) {
1067. // The INVERSE color is used so circles alternate white/black
1068. display.fillCircle(display.width() / 2, display.height() / 2, i, SSD1306_INVERSE);
1069. display.display(); // Update screen with each newly-drawn circle
1070. delay(1);
1071. }
1073. delay(2000);
1074. }
1076. void testdrawroundrect(void) {
1077. display.clearDisplay();
1079. for(int16_t i=0; i<display.height()/2-2; i+=2) {
1080. display.drawRoundRect(i, i, display.width()-2*i, display.height()-2*i,
1081. display.height()/4, SSD1306_WHITE);
1082. display.display();
1083. delay(1);
1084. }
1086. delay(2000);
1087. }
1089. void testfillroundrect(void) {
1090. display.clearDisplay();
1092. for(int16_t i=0; i<display.height()/2-2; i+=2) {
1093. // The INVERSE color is used so round-rects alternate white/black
1094. display.fillRoundRect(i, i, display.width()-2*i, display.height()-2*i,
1095. display.height()/4, SSD1306_INVERSE);
1096. display.display();
1097. delay(1);
1098. }
1100. delay(2000);
1101. }
1103. void testdrawtriangle(void) {
1104. display.clearDisplay();
1106. for(int16_t i=0; i<max(display.width(),display.height())/2; i+=5) {
1107. display.drawTriangle(
1108. display.width()/2 , display.height()/2-i,
1109. display.width()/2-i, display.height()/2+i,
1110. display.width()/2+i, display.height()/2+i, SSD1306_WHITE);
1111. display.display();
1112. delay(1);
1113. }
1115. delay(2000);
1116. }
1118. void testfilltriangle(void) {
1119. display.clearDisplay();
1121. for(int16_t i=max(display.width(),display.height())/2; i>0; i-=5) {
1122. // The INVERSE color is used so triangles alternate white/black
1123. display.fillTriangle(
1124. display.width()/2 , display.height()/2-i,
1125. display.width()/2-i, display.height()/2+i,
1126. display.width()/2+i, display.height()/2+i, SSD1306_INVERSE);
1127. display.display();
1128. delay(1);
1129. }
1131. delay(2000);
1132. }
1134. void testdrawchar(void) {
1135. display.clearDisplay();
1137. display.setTextSize(1); // Normal 1:1 pixel scale
1138. display.setTextColor(SSD1306_WHITE); // Draw white text
1139. display.setCursor(0, 0); // Start at top-left corner
1140. display.cp437(true); // Use full 256 char 'Code Page 437' font
1142. // Not all the characters will fit on the display. This is normal.
1143. // Library will draw what it can and the rest will be clipped.
1144. for(int16_t i=0; i<256; i++) {
1145. if(i == '\n') display.write(' ');
1146. else display.write(i);
1147. }
1149. display.display();
1150. delay(2000);
1151. }
1153. void testdrawstyles(void) {
1154. display.clearDisplay();
1156. display.setTextSize(1); // Normal 1:1 pixel scale
1157. display.setTextColor(SSD1306_WHITE); // Draw white text
1158. display.setCursor(0,0); // Start at top-left corner
1159. display.println(F("Hello, world!"));
1161. display.setTextColor(SSD1306_BLACK, SSD1306_WHITE); // Draw 'inverse' text
1162. display.println(3.141592);
1164. display.setTextSize(2); // Draw 2X-scale text
1165. display.setTextColor(SSD1306_WHITE);
1166. display.print(F("0x")); display.println(0xDEADBEEF, HEX);
1168. display.display();
1169. delay(2000);
1170. }
1172. void testscrolltext(void) {
1173. display.clearDisplay();
1175. display.setTextSize(2); // Draw 2X-scale text
1176. display.setTextColor(SSD1306_WHITE);
1177. display.setCursor(10, 0);
1178. display.println(F("scroll"));
1179. display.display(); // Show initial text
1180. delay(100);
1182. // Scroll in various directions, pausing in-between:
1183. display.startscrollright(0x00, 0x0F);
1184. delay(2000);
1185. display.stopscroll();
1186. delay(1000);
1187. display.startscrollleft(0x00, 0x0F);
1188. delay(2000);
1189. display.stopscroll();
1190. delay(1000);
1191. display.startscrolldiagright(0x00, 0x07);
1192. delay(2000);
1193. display.startscrolldiagleft(0x00, 0x07);
1194. delay(2000);
1195. display.stopscroll();
1196. delay(1000);
1197. }
1199. void testdrawbitmap(void) {
1200. display.clearDisplay();
1202. display.drawBitmap(
1203. (display.width() - LOGO_WIDTH ) / 2,
1204. (display.height() - LOGO_HEIGHT) / 2,
1205. logo_bmp, LOGO_WIDTH, LOGO_HEIGHT, 1);
1206. display.display();
1207. delay(1000);
1208. }
1210. #define XPOS 0 // Indexes into the 'icons' array in function below
1211. #define YPOS 1
1212. #define DELTAY 2
1214. void testanimate(const uint8_t *bitmap, uint8_t w, uint8_t h) {
1215. int8_t f, icons[NUMFLAKES][3];
1217. // Initialize 'snowflake' positions
1218. for(f=0; f< NUMFLAKES; f++) {
1219. icons[f][XPOS] = random(1 - LOGO_WIDTH, display.width());
1220. icons[f][YPOS] = -LOGO_HEIGHT;
1221. icons[f][DELTAY] = random(1, 6);
1222. Serial.print(F("x: "));
1223. Serial.print(icons[f][XPOS], DEC);
1224. Serial.print(F(" y: "));
1225. Serial.print(icons[f][YPOS], DEC);
1226. Serial.print(F(" dy: "));
1227. Serial.println(icons[f][DELTAY], DEC);
1228. }
1230. for(int i=1;i<3;i++) { // changed to loop 2 times from Loop forever...
1231. display.clearDisplay(); // Clear the display buffer
1233. // Draw each snowflake:
1234. for(f=0; f< NUMFLAKES; f++) {
1235. display.drawBitmap(icons[f][XPOS], icons[f][YPOS], bitmap, w, h, SSD1306_WHITE);
1236. }
1238. display.display(); // Show the display buffer on the screen
1239. delay(200); // Pause for 1/10 second
1241. // Then update coordinates of each flake...
1242. for(f=0; f< NUMFLAKES; f++) {
1243. icons[f][YPOS] += icons[f][DELTAY];
1244. // If snowflake is off the bottom of the screen...
1245. if (icons[f][YPOS] >= display.height()) {
1246. // Reinitialize to a random position, just off the top
1247. icons[f][XPOS] = random(1 - LOGO_WIDTH, display.width());
1248. icons[f][YPOS] = -LOGO_HEIGHT;
1249. icons[f][DELTAY] = random(1, 6);
1250. }
1251. }
1252. }
1253. }

KNODE 21-SLAVE DEV SOURCE CODE (PASSED)

Source Code
1. // ***********************************************************************
2. // Nov 27, 2022
3. // Placing interrupt in loop() allows for successful restart without
4. // master node interrupt side effects; tested with nodes 1 and 3
5. // on master node may need to set longer time delay for greater
6. // reliability of restart for all nodes
7. // -----------------------------------------------------------------
8. // November 20, 2022
9. // changed interrupt attachment to loop() rather than setup()
10. // and changed state from CHANGING to FALLING
11. // goal - is to have master node restart and interrupt work together
12. // master node restart works
13. // ***********************************************************************
14. // KNODE 2.0 - August 26, 2022
15. // readRegister and writeRegister works!
16. // ***********************************************************************
17. // Oct 3, 2022 - r19
18. // Slave test module 1
19. // Sept 29, 2022 - r18
20. // Dual register problem solved
21. // Solution - each register needs its' own clockPin and latchPin lines
22. // - using latchPinCSR and clockPin2 for register 0
23. // - using latchPin and clockPin for register 1
24. // Sept 27, 2022 - r18
25. // new masking works (nodeID<<4)+ (regID)
26. // but only correct read of register 1 in Node 0 state, all other states gives incorrect value
27. // Sept 23, 2022 - r17
28. // initial round robin test
29. // round robit for mux node selects works, but readRegister1() has value error in loop test
30. // cross talk between reg0 and reg1 due to *OE (active low) control [gnd vd *S0]
31. // --- idea to use d0/other pin for output enable (OE) control rather than mux
32. // --- or use 8255 peripheral chip
33. // --- cant have two or more *OE's active at a time, only 1
34. // --- need to control which register *OE is active at a time
35. // --- for round robin to read proper register
36. //
37. // round robin works for node selection with mux (*OE register control needs addition)
38. // ***********************************************************************
39. // Sept 19, 2022 - r16
40. // Using AdaFruit display monitor within interrupt
41. // Prep for round-robin master/slave test
42. // loop and data xfer tests works.
43. // Sept 13, 2022- r15
44. // ISR routine works and gets proper value from setup of register 1
45. // (need to think of using intell 8255 for easier peripheral control rather homebrew method being used)
46. // add link to mux *S0, *S1(reg1), *S2(reg2), etc for multiple register control past reg 1
47. // dual D4 link from two processors work
48. // -----------------------------------------------------------------------
49. // to write register 1
50. // use:
51. // writeRegister0(1);
52. // writeRegister1(data);
53. // -----------------------------------------------------------------------
54. // to read register 1
55. // use:
56. // value=readRegister1();
57. // Note --- if writeRegister0(1) is used will read wrong value
58. // --- glitch still exists
59. // ***********************************************************************
60. // Sept 10, 2022- r12
61. // Added bus control, D0, which checks is bus is availble, D0=1, or busy, D0=0
62. // works with testModule5()
63. // Added invalid register access error message as default: statement
64. // Added "-r12" terminator in screen msgs so to know which version of Master code is running
65. // ***********************************************************************
66. // Sept 6, 2022 - r11
67. // Need 74157 for 1 to 4 selector for CLK pin to avoid activating all pins for more than 1 register
68. // work around is using D4 on second CLK pin
69. // Sept 6, 2022 - r9
70. // Update for 4 latch registers and shared CLK, Din, Dout
71. //
72. // *****************************************************************
73. // * Multi Bus Setup Constants
74. // ****************************************************************
75. //
76. // Absolute pin setup as D3 is for use with esp8266 (NODE 1.0-12E)
77. //int latchPin = D3; // Reg1 --- gpio 0 pin 11 on 74595 chip, registers 1-3
78. //int latchPinCSR = D4; // Reg0 --- gpio 2 pin 11 on register 0
79. //int latchPinReg2= 16; // Reg2 --- gpio 16, D0 on esp8266
80. //int latchPinReg3= 10; // Reg3 --- gpio 10, SD3 on esp8266
81. //
82. //int clockPin = D5; // gpio 14 pin 12 on 74595 chip
83. //int dataPinOut = D7; // gpio 13 pin 14 on 74595 chip;
84. //int dataPinIn = D6; // gpio 12 pin 9 on 74595 chip
85. // int interruptPin= D8; // gpio 15
86. //
87. // int clearBus = 0;
88. // *** END Multi Bus Setup Constants ***
89. // ************************************************************
90. // Sept 3, 2022
91. // Revision 8
92. // Code for readRegister1 works, need to use MUX *S0 attached to OE* (pin 13
93. // to control output
94. // *S0 means *S0 is active low
95. // ***********************************************************************
96. // Sept 1, 2022
97. // Second MUX works. I/O routines work with proper formatting
98. // ***********************************************************************
99. // August 31 --- Version R7
100. // CSR (Control Status Register) work properly with 74138 decoders for register selection
101. // --- next test: read/write from registers 1 to 4
102. //
103. // ***********************************************************************
104. // August 24, 2022
105. // Master Mode of SPI-1-R4
106. // =======================================================================
107. // August 22, 2022
108. // SPI-1-r3 with OLED 128x64, device ID using shift registe 74HC595, and SPI
109. // Multiple Bus Class Use
110. // (C) 2022 Diana Kanecki, All Rights Reserved
111. // Diana Kanecki, DM(ABD), MBA, ACS, Bio. Sci.
112. //
113. // **********************************************************************
115. /**************************************************************************
116. This is an example for our Monochrome OLEDs based on SSD1306 drivers
118. Pick one up today in the adafruit shop!
119. ------> http://www.adafruit.com/category/63_98
121. This example is for a 128x32 pixel display using I2C to communicate
122. 3 pins are required to interface (two I2C and one reset).
124. Adafruit invests time and resources providing this open
125. source code, please support Adafruit and open-source
126. hardware by purchasing products from Adafruit!
128. Written by Limor Fried/Ladyada for Adafruit Industries,
129. with contributions from the open source community.
130. BSD license, check license.txt for more information
131. All text above, and the splash screen below must be
132. included in any redistribution.
133. **************************************************************************/
135. //#include <SPI.h>
136. #include <Wire.h>
137. #include <Adafruit_GFX.h>
138. #include <Adafruit_SSD1306.h>
140. #define SCREEN_WIDTH 128 // OLED display width, in pixels
141. //#define SCREEN_HEIGHT 32 // OLED display height, in pixels
142. #define SCREEN_HEIGHT 64 // OLED display height, in pixels (determines character height - changable for better reading)
144. // Declaration for an SSD1306 display connected to I2C (SDA, SCL pins)
145. // The pins for I2C are defined by the Wire-library.
146. // On an arduino UNO: A4(SDA), A5(SCL)
147. // On an arduino MEGA 2560: 20(SDA), 21(SCL)
148. // On an arduino LEONARDO: 2(SDA), 3(SCL), ...
149. #define OLED_RESET -1 // Reset pin # (or -1 if sharing Arduino reset pin)
150. //#define SCREEN_ADDRESS 0x3C ///< See datasheet for Address; 0x3D for 128x64, 0x3C for 128x32
151. #define SCREEN_ADDRESS 0x3C
152. Adafruit_SSD1306 display(SCREEN_WIDTH, SCREEN_HEIGHT, &Wire, OLED_RESET);
154. #define NUMFLAKES 10 // Number of snowflakes in the animation example
156. #define LOGO_HEIGHT 16
157. #define LOGO_WIDTH 16
158. static const unsigned char PROGMEM logo_bmp[] =
159. { 0b00000000, 0b11000000,
160. 0b00000001, 0b11000000,
161. 0b00000001, 0b11000000,
162. 0b00000011, 0b11100000,
163. 0b11110011, 0b11100000,
164. 0b11111110, 0b11111000,
165. 0b01111110, 0b11111111,
166. 0b00110011, 0b10011111,
167. 0b00011111, 0b11111100,
168. 0b00001101, 0b01110000,
169. 0b00011011, 0b10100000,
170. 0b00111111, 0b11100000,
171. 0b00111111, 0b11110000,
172. 0b01111100, 0b11110000,
173. 0b01110000, 0b01110000,
174. 0b00000000, 0b00110000 };
176. // *****************************************************************
177. // * Multi Bus Setup Constants
178. // ****************************************************************
180. // Absolute pin setup as D3 is for use with esp8266 (NODE 1.0-12E)
181. int latchPin = D3; // Reg1 --- gpio 0 pin 11 on 74595 chip, registers 1-3
182. int latchPinCSR = D4; // Reg0 --- gpio 2 pin 11 on register 0
183. //int latchPinReg2= 16; // Reg2 --- gpio 16, D0 on esp8266
184. //int latchPinReg3= 10; // Reg3 --- gpio 10, SD3 on esp8266
185. //
186. int clockPin = D5; // gpio 14 pin 12 on 74595 chip
187. //int clockPin2 = 10; // pin12 on 74595 chip
188. int dataPinOut = D7; // gpio 13 pin 14 on 74595 chip;
189. int clockPin2 = D9; // 10; // sd3
190. int dataPinIn = D6; // gpio 12 pin 9 on 74595 chip
191. int interruptPin= D8; // gpio 15
192. int busPin = D0;
193. //
194. int clearBus = 0;
195. int maxRegisters = 1;
196. int OEReg1 = 10; // OK - added 9/22/2022 sd3
198. // *** END Multi Bus Setup Constants ***
200. volatile int j=0;
201. volatile int NodeId=0;
202. char buff[100]= "Hello from Host\n\0";
203. volatile int index1;
204. volatile bool receivedone;
205. //int int1 = D8; //
206. int slaveLatch = D8;
207. int lastValue1 = 0;
208. int lineCount1 = 0;
209. int nullRegister = 3;
211. unsigned long button_time = 0;
212. unsigned long last_button_time = 0;
213. int y = 0;
214. bool ledToggle = false;
215. int intValueRd=0;
216. bool firstLoop = true;
218. void testMode() {
219. /*
220. testdrawline(); // Draw many lines
222. testdrawrect(); // Draw rectangles (outlines)
224. testfillrect(); // Draw rectangles (filled)
226. testdrawcircle(); // Draw circles (outlines)
228. testfillcircle(); // Draw circles (filled)
230. testdrawroundrect(); // Draw rounded rectangles (outlines)
232. testfillroundrect(); // Draw rounded rectangles (filled)
234. testdrawtriangle(); // Draw triangles (outlines)
236. testfilltriangle(); // Draw triangles (filled)
238. testdrawchar(); // Draw characters of the default font
240. testdrawstyles(); // Draw 'stylized' characters
242. testscrolltext(); // Draw scrolling text
244. testdrawbitmap(); // Draw a small bitmap image
246. // Invert and restore display, pausing in-between
247. display.invertDisplay(true);
248. delay(1000);
249. display.invertDisplay(false);
250. delay(1000);
252. testanimate(logo_bmp, LOGO_WIDTH, LOGO_HEIGHT); // Animate bitmaps
253. */
255. }
257. void setup() {
258. Serial.begin(9600);
259. pinMode(latchPin,OUTPUT);
260. pinMode(clockPin,OUTPUT);
261. //pinMode(clockPin2,OUTPUT);
262. pinMode(latchPinCSR,OUTPUT);
263. //pinMode(latchPinReg2,OUTPUT);
265. //pinMode(latchPinReg3,OUTPUT);
266. pinMode(dataPinOut,OUTPUT);
267. pinMode(clockPin2,OUTPUT);
268. digitalWrite(clockPin2,LOW);
269. pinMode(dataPinIn,INPUT);
271. pinMode(busPin,OUTPUT);
272. digitalWrite(busPin,LOW);
273. pinMode(busPin,LOW);
275. // *******************************************************************************
276. // *** Multibus setup code - quietBus()
277. // *******************************************************************************
278. digitalWrite(latchPin,LOW);
279. shiftOut(dataPinOut,clockPin, MSBFIRST,clearBus); // clear bus
280. digitalWrite(latchPin,HIGH);
282. //digitalWrite(latchPinReg2,HIGH);
283. //digitalWrite(latchPinReg3,HIGH);
284. // *** END Multibus setup code ***************************************************
287. // SSD1306_SWITCHCAPVCC = generate display voltage from 3.3V internally
288. if(!display.begin(SSD1306_SWITCHCAPVCC, SCREEN_ADDRESS)) {
289. Serial.println(F("SSD1306 allocation failed"));
290. for(;;); // Don't proceed, loop forever
291. }
293. // Show initial display buffer contents on the screen --
294. // the library initializes this with an Adafruit splash screen.
295. display.display();
296. delay(2000); // Pause for 2 seconds
298. // Clear the buffer
299. display.clearDisplay();
301. // Draw a single pixel in white
302. display.drawPixel(10, 10, SSD1306_WHITE);
304. // Show the display buffer on the screen. You MUST call display() after
305. // drawing commands to make them visible on screen!
306. display.display();
307. delay(2000);
308. // display.display() is NOT necessary after every single drawing command,
309. // unless that's what you want...rather, you can batch up a bunch of
310. // drawing operations and then update the screen all at once by calling
311. // display.display(). These examples demonstrate both approaches...
313. // testMode();
315. // ************************************************************
316. // *** Multibus Setup Codes
317. // ************************************************************
319. index1=0;
320. receivedone=false;
322. // Start at top-left corner
323. display.clearDisplay();
325. display.setTextSize(1); // Normal 1:1 pixel scale
326. display.setTextColor(SSD1306_WHITE); // Draw white text
327. display.setCursor(0,0);
328. lineCount1=0;
330. //writeRegister0(1);
331. //writeRegister1(5);
332. //delay(1000);
333. //writeRegister0(0);
334. }
336. ICACHE_RAM_ATTR void testInt8(){
338. int value = 0;
339. noInterrupts();
340. button_time = millis();
341. //check to see if increment() was called in the last 250 milliseconds
342. if (button_time - last_button_time > 250){
343. // writeRegister0(1); // added 9/23/2022 to select reg1
344. value = readRegister1();
345. ledToggle = true;
346. intValueRd = value;
347. Serial.print("In Interupt r19- ");
348. Serial.print(" value retrieved is ");
349. Serial.println(value);
350. Serial.println();
351. // writeRegister1(value); added 9/23/2022
352. last_button_time = button_time;
354. }
355. interrupts();
356. }
358. void loop() {
359. Serial.print("in Slave Node 1 - r21 - ");
360. Serial.println(j);
361. lineCount1=0;
362. display.clearDisplay();
363. display.setCursor(0,0);
364. display.display();
366. writeStr1("Hello-Nd 3/22 ");
367. writeInt1(j);
368. writeLn1();
369. display.display();
370. delay(1000);
372. if (j==3){
373. lineCount1=0;
374. display.clearDisplay();
375. display.setCursor(0,0);
376. display.display();
378. writeStr1("---Init Int");
379. writeLn1();
380. delay(1000);
381. for (int k=1; k<5;k++){
382. writeInt1(k);
383. writeStr1(" ");
384. delay(1000);
385. }
386. pinMode(15,INPUT_PULLUP);
387. // use GPIO 15 -> D8
388. attachInterrupt(digitalPinToInterrupt(D8),testInt8,FALLING);
389. firstLoop=false;
390. }
391. writeLn1();
392. display.display();
393. if (ledToggle)
394. {
395. display.clearDisplay();
396. display.setCursor(0,0);
397. display.display();
398. writeStr1("Process Int r19 ");
399. writeLn1();
400. writeStr1("Value read->");
401. writeInt1(intValueRd);
402. writeLn1();
403. display.display();
404. ledToggle=false;
405. delay(2000);
406. };
408. delay(1000);
409. j++;
410. NodeId= NodeId++;
411. // i = i % 4;
412. }
414. // **************************************************
415. // *** Register Routines
416. // **************************************************
417. void writeRegister0(int dataOut)
418. {
419. // Aug 31, 2022 - verified to work for register 0
420. // for use with any SIPO register as 74595 and 74165
422. //digitalWrite(latchPin,LOW); // OK - added 9/23/2022 to deselect reg1
423. digitalWrite(latchPinCSR,LOW);
424. shiftOut(dataPinOut,clockPin2, MSBFIRST,dataOut);
425. digitalWrite(latchPinCSR,HIGH);
426. //digitalWrite(latchPin,HIGH);
428. }
430. void writeRegister1(int dataOut)
431. {
432. // verified - Sept 3, 2022 - to work with 74595 chip
433. // Serial.println("... in writeRegister1()");
435. digitalWrite(latchPinCSR,LOW);
437. // works Sept 3, 2022
438. digitalWrite(latchPin,LOW);
439. shiftOut(dataPinOut,clockPin, MSBFIRST,dataOut);
440. digitalWrite(latchPin,HIGH);
442. digitalWrite(latchPinCSR,HIGH);
444. }
446. /*
447. void writeRegister2(int dataOut)
448. {
449. // Sept 6, 2022 --- Need to test
450. // Serial.println("... in writeRegister2()");
452. // works Sept 3, 2022
453. digitalWrite(latchPinReg2,LOW);
454. shiftOut(dataPinOut,clockPin, MSBFIRST,dataOut);
455. digitalWrite(latchPinReg2,HIGH);
456. }
458. void writeRegister3(int dataOut)
459. {
460. // Sept 6, 2022 --- need to test
461. // Serial.println("... in writeRegister2()");
463. // works Sept 3, 2022
464. digitalWrite(latchPinReg3,LOW);
465. shiftOut(dataPinOut,clockPin, MSBFIRST,dataOut);
466. digitalWrite(latchPinReg3,HIGH);
467. }
468. */
470. void writeCtrlRegToBus(int dataOut)
471. {
472. //digitalWrite(busPin,LOW);
473. writeRegister0(dataOut);
474. //digitalWrite(busPin,HIGH);
475. }
477. int readRegister0()
478. {
479. // Aug 31, 2022 - verified to work for register 0
480. // for special use with 74595 shift register SIPO
481. int value = 0;
482. int bitOrder = MSBFIRST;
484. digitalWrite(latchPin,LOW); // OK -added 9/23/2022 to block access to reg 0 while rd reg 1
486. for (int i = 0; i < 8; ++i) {
487. if (bitOrder == LSBFIRST)
488. value |= digitalRead(dataPinIn) << i;
489. else
490. value |= digitalRead(dataPinIn) << (7 - i);
491. digitalWrite(clockPin2, HIGH);
492. digitalWrite(clockPin2, LOW);
493. }
494. digitalWrite(latchPin,HIGH);
495. return(value);
496. }
498. int readRegister1()
499. {
500. // Sept 6, 2022 --- need to test
501. // need decoder for more than one register 74153
502. // because clk pin activates all at same time
504. int value = 0;
505. int bitOrder = MSBFIRST;
507. //Serial.println(" ... in readRegister1()");
509. digitalWrite(latchPinCSR,LOW); // OK-added 9/23/2022 block reading register 0
511. for (int i = 0; i < 8; ++i) {
512. if (bitOrder == LSBFIRST)
513. value |= digitalRead(dataPinIn) << i;
514. else
515. value |= digitalRead(dataPinIn) << (7 - i);
517. digitalWrite(latchPin,LOW);
518. digitalWrite(clockPin, HIGH);
519. digitalWrite(clockPin, LOW);
520. digitalWrite(latchPin,HIGH);
521. }
523. writeRegister1(value); // added 9/27/2022
524. digitalWrite(latchPinCSR,HIGH);
525. return(value);
526. }
528. int readRegister2()
529. {
530. // Sept 6, 2022 --- Need to test
531. // need decoder for more than one register 74153
532. // because clk pin activates all at same time
533. int value = 0;
534. int bitOrder = MSBFIRST;
536. //Serial.println(" ... in readRegister2()");
538. if (2 <= maxRegisters)
539. {
541. for (int i = 0; i < 8; ++i) {
542. if (bitOrder == LSBFIRST)
543. value |= digitalRead(dataPinIn) << i;
544. else
545. value |= digitalRead(dataPinIn) << (7 - i);
547. digitalWrite(clockPin, HIGH);
548. digitalWrite(clockPin, LOW);
549. }
550. }
551. else value=0;
553. return(value);
554. }
556. int readRegister3()
557. {
558. // Sept 6, 2022 --- Need to test
559. // need decoder for more than one register 74153
560. // because clk pin activates all at same time
561. int value = 0;
562. int bitOrder = MSBFIRST;
564. if (3 <= maxRegisters)
565. {
566. for (int i = 0; i < 8; ++i) {
567. if (bitOrder == LSBFIRST)
568. value |= digitalRead(dataPinIn) << i;
569. else
570. value |= digitalRead(dataPinIn) << (7 - i);
572. //digitalWrite(latchPinReg3,LOW);
573. digitalWrite(clockPin, HIGH);
574. digitalWrite(clockPin, LOW);
575. //digitalWrite(latchPinReg3,HIGH);
576. }
577. }
578. else value=0;
579. return(value);
580. }
582. // *****************************************************
583. // *** I/O Routines
584. // *****************************************************
585. void writeInt1( int val){
586. // Sept 1, 2022 - verified to work with formatting
587. display.print(val);
588. display.display();
589. }
591. void writeStr1( char str1[]){
592. // Sept 1, 2022 - verified to work with formatting
593. display.print(str1);
594. display.display();
595. }
597. void writeLnStr1( char str1[]){
598. // Sept 1, 2022 - verified to work with formatting
599. display.println(str1);
600. display.display();
601. lineCount1++;
602. if (lineCount1 > 6)
603. {
604. delay(2000);
605. display.clearDisplay();
606. display.setCursor(0,0);
607. display.display();
608. lineCount1=0;
609. }
610. display.clearDisplay();
611. display.display();
612. }
614. void writeLn1() {
615. // Sept 1, 2022 - verified to work with formatting
616. display.println();
617. display.display();
618. lineCount1++;
619. if (lineCount1 > 6)
620. {
621. delay(2000);
622. display.clearDisplay();
623. display.setCursor(0,0);
624. display.display();
625. lineCount1=0;
626. }
627. }
629. // ****************************************************************
630. // *** Test Routines
631. // ****************************************************************
632. void testModule1()
633. {
634. // verified to work Aug 28, 2022
635. /*
636. for(int k=0; ((k < sizeof buff) && (buff[k]!=0)); k++ ){
637. Serial.print("Sending char(");
638. Serial.print((char)buff[k]);
639. Serial.println(")");
640. display.setCursor(0,20); // Start at top-left corner
641. display.print(F("Sending ch ("));
642. display.print(buff[k]);
643. display.print(") ");
644. display.println(k);
645. display.display();
647. digitalWrite(slaveLatch,LOW); // slave select ON
648. digitalWrite(slaveLatch,HIGH); // slave select OFF
649. delay(1000);
650. }
651. */
652. /*
653. display.setTextColor(SSD1306_WHITE); // Draw white text
654. display.setCursor(0,20); // Start at top-left corner
655. display.print(buff);
656. display.print(j);
657. display.println();
658. display.display();
659. */
660. /*
661. if (receivedone)
662. {
663. buff[index1]= 0;
664. display.setTextSize(1); // Normal 1:1 pixel scale
665. display.setTextColor(SSD1306_WHITE); // Draw white text
666. display.setCursor(3,0); // Start at top-left corner
667. display.print(F("Msg from Host! "));
668. display.print(buff);
669. display.println();
670. display.display();
672. index1=0;
673. receivedone=false;
674. }
675. */
676. // *************************************************************
677. // *** Device ID Register Code using 74HC595
678. // *************************************************************
680. // Device ID Register Control Code for Master Node
681. for (int i=0; i<256; i++) {
682. //display.setCursor(0,20);
683. display.print("Writing ... ");
684. display.println(i);
685. //display.println();
686. display.display();
687. lineCount1++;
688. Serial.print("Writing ...");
689. Serial.println(i);
690. writeRegister0(i);
692. lastValue1 = readRegister0();
694. //display.setCursor(0,30);
695. display.print("Reading ... ");
696. display.print(lastValue1);
697. display.println();
698. display.display();
699. lineCount1++;
700. Serial.print("Reading LastValue =");
701. Serial.println(lastValue1);
702. Serial.print("LineCount1 is ");
703. Serial.println(lineCount1);
704. Serial.println("\n");
705. // if ((i % 4) == 0)
706. // if ((lineCount1 & 8) == 0) // display first two entries then clears
707. if (((lineCount1 % 8) == 0) || (lineCount1 > 8))
708. {
709. delay(1000);
710. display.clearDisplay();
711. display.setCursor(0,0);
712. display.display();
713. lineCount1=0;
714. }
715. delay(1000);
716. }
717. }
719. void testModule2()
720. {
721. // updated Sept 1, 2022 -- added test for mux in 8 to 12
722. int lastValue1;
724. writeStr1("IN testModule2() ");
725. writeLn1();
726. delay(1000);
727. for (int i=0; i<4;i++)
728. {
729. writeRegister0(i);
731. writeStr1("Writing ... ");
732. writeInt1(i);
733. //display.println();
734. writeLn1();
736. Serial.print("Writing ...");
737. Serial.print(i);
739. lastValue1 = readRegister0();
741. writeStr1("Reading ... ");
742. writeInt1(lastValue1);
743. //display.println();
744. writeLn1();
746. Serial.print(" Reading ...");
747. Serial.print(lastValue1);
748. Serial.print(" LineCount1 is ");
749. Serial.println(lineCount1);
750. Serial.println();
751. delay(1000);
752. }
753. /*
754. for (int i=8; i<12;i++)
755. {
756. writeRegister0(i);
758. writeStr1("Writing ... ");
759. writeInt1(i);
760. //display.println();
761. writeLn1();
763. Serial.print("Writing ...");
764. Serial.println(i);
765. Serial.print("LineCount1 is ");
766. Serial.println(lineCount1);
767. Serial.println("\n");
768. delay(1000);
769. }
770. */
771. }
773. void testModule3()
774. {
775. // sept 6, 2022 --- verified to work
776. // started Sept 3, 2022 -- added test for mux in 8 to 12
777. int lastValue=0;
779. writeStr1("IN testModule3() ");
780. writeLn1();
781. delay(1000);
782. for (int i=0; i<16;i++)
783. {
784. writeRegister0(1); // added Spet 13, 2022 -- cant work embedded in writeRegister0()
785. writeRegister1(i);
787. writeStr1("Writing ... ");
788. writeInt1(i);
789. //display.println();
790. writeLn1();
792. Serial.print("Writing ...");
793. Serial.println(i);
794. Serial.print("LineCount1 is ");
795. Serial.println(lineCount1);
796. Serial.println("\n");
797. lastValue1 = readRegister1();
799. Serial.print("Reading ...");
800. Serial.println(lastValue1);
801. Serial.println();
802. //display.setCursor(0,30);
803. writeStr1("Reading ... ");
804. writeInt1(lastValue1);
805. writeLn1();
806. display.display();
808. writeRegister1(i);
809. delay(1000);
810. }
811. }
813. void testModule5(int regNum)
814. {
816. // started Sept 3, 2022 -- added test for mux in 8 to 12
817. int lastValue=0;
818. int busStatus = 1;
820. writeStr1("IN testModule5()-r12 ");
821. writeLn1();
822. delay(1000);
824. busStatus=digitalRead(busPin);
825. while (busStatus !=0){
826. writeStr1(" ... Bus Busy, Waiting");
827. writeLn1();
828. delay(1000);
829. busStatus = digitalRead(busPin);
830. }
831. writeStr1(" ... Bus Ready");
832. writeLn1();
833. for (int i=0; i<16;i++)
834. {
835. switch(regNum){
836. case 0: writeRegister0(i);
837. break;
838. case 1:
839. writeRegister0(1);
840. writeRegister1(i);
841. break;
842. /*
843. case 2:
844. writeRegister0(2);
845. writeRegister2(i);
846. break;
847. case 3:
848. writeRegister0(3);
849. writeRegister3(i);
850. break;
851. */
852. default:
853. writeStr1(" ... INV reg ");
854. writeRegister0(regNum);
855. delay(1000);
856. writeInt1(regNum);
857. writeLn1();
858. break;
859. }
860. //writeRegister0(0);
861. //delay(1000);
863. writeStr1("Wr Reg ");
864. writeInt1(regNum);
865. writeStr1(" ->");
866. writeInt1(i);
867. //display.println();
868. writeLn1();
870. Serial.print("Writing Reg ");
871. Serial.print(regNum);
872. Serial.print("...");
873. Serial.print(i);
874. Serial.print(" LineCount1 is ");
875. Serial.print(lineCount1);
876. Serial.print(" Register->");
877. Serial.print(regNum);
878. switch(regNum){
879. case 0: lastValue1=readRegister0();
880. break;
881. case 1:
882. //writeRegister0(1);
883. lastValue1=readRegister1();
884. break;
885. /*
886. case 2: lastValue1=readRegister2();
887. break;
888. case 3: lastValue1=readRegister3();
889. break;
890. */
891. default:
892. writeStr1(" ... INV reg ");
893. writeRegister0(regNum);
894. delay(1000);
895. writeInt1(regNum);
896. writeLn1();
897. lastValue1 =0;
898. break;
899. }
900. //writeRegister0(0);
901. //delay(1000);
902. // lastValue1=readRegister1();
904. Serial.print(" Reading ...");
905. Serial.println(lastValue1);
906. Serial.println();
907. //display.setCursor(0,30);
908. writeStr1("Reading ... ");
909. writeInt1(lastValue1);
910. writeLn1();
911. display.display();
913. switch(regNum){
914. case 0: writeRegister0(i);
915. break;
916. case 1:
917. writeRegister0(1);
918. writeRegister1(i);
919. break;
920. /*
921. case 2: writeRegister2(i);
922. break;
923. case 3: writeRegister3(i);
924. break;
925. */
926. default:
927. writeStr1(" ... INV reg ");
928. writeRegister0(regNum);
929. delay(1000);
930. writeInt1(regNum);
931. writeLn1();
932. break;
933. }
934. //writeRegister0(0);
935. //delay(1000);
936. }
937. }
939. /*
940. void testModule4()
941. {
942. // Sept6, 2022 --- test module 4 verified to work
944. Serial.println("Hello from testModule4()");
945. digitalWrite(latchPinReg2,HIGH);
946. digitalWrite(latchPinReg3,LOW);
947. delay(1000);
948. digitalWrite(latchPinReg2,LOW);
949. digitalWrite(latchPinReg3,HIGH);
950. delay(1000);
951. }
953. */
955. void testdrawline() {
956. int16_t i;
958. display.clearDisplay(); // Clear display buffer
960. for(i=0; i<display.width(); i+=4) {
961. display.drawLine(0, 0, i, display.height()-1, SSD1306_WHITE);
962. display.display(); // Update screen with each newly-drawn line
963. delay(1);
964. }
965. for(i=0; i<display.height(); i+=4) {
966. display.drawLine(0, 0, display.width()-1, i, SSD1306_WHITE);
967. display.display();
968. delay(1);
969. }
970. delay(250);
972. display.clearDisplay();
974. for(i=0; i<display.width(); i+=4) {
975. display.drawLine(0, display.height()-1, i, 0, SSD1306_WHITE);
976. display.display();
977. delay(1);
978. }
979. for(i=display.height()-1; i>=0; i-=4) {
980. display.drawLine(0, display.height()-1, display.width()-1, i, SSD1306_WHITE);
981. display.display();
982. delay(1);
983. }
984. delay(250);
986. display.clearDisplay();
988. for(i=display.width()-1; i>=0; i-=4) {
989. display.drawLine(display.width()-1, display.height()-1, i, 0, SSD1306_WHITE);
990. display.display();
991. delay(1);
992. }
993. for(i=display.height()-1; i>=0; i-=4) {
994. display.drawLine(display.width()-1, display.height()-1, 0, i, SSD1306_WHITE);
995. display.display();
996. delay(1);
997. }
998. delay(250);
1000. display.clearDisplay();
1002. for(i=0; i<display.height(); i+=4) {
1003. display.drawLine(display.width()-1, 0, 0, i, SSD1306_WHITE);
1004. display.display();
1005. delay(1);
1006. }
1007. for(i=0; i<display.width(); i+=4) {
1008. display.drawLine(display.width()-1, 0, i, display.height()-1, SSD1306_WHITE);
1009. display.display();
1010. delay(1);
1011. }
1013. delay(2000); // Pause for 2 seconds
1014. }
1016. void testdrawrect(void) {
1017. display.clearDisplay();
1019. for(int16_t i=0; i<display.height()/2; i+=2) {
1020. display.drawRect(i, i, display.width()-2*i, display.height()-2*i, SSD1306_WHITE);
1021. display.display(); // Update screen with each newly-drawn rectangle
1022. delay(1);
1023. }
1025. delay(2000);
1026. }
1028. void testfillrect(void) {
1029. display.clearDisplay();
1031. for(int16_t i=0; i<display.height()/2; i+=3) {
1032. // The INVERSE color is used so rectangles alternate white/black
1033. display.fillRect(i, i, display.width()-i*2, display.height()-i*2, SSD1306_INVERSE);
1034. display.display(); // Update screen with each newly-drawn rectangle
1035. delay(1);
1036. }
1038. delay(2000);
1039. }
1041. void testdrawcircle(void) {
1042. display.clearDisplay();
1044. for(int16_t i=0; i<max(display.width(),display.height())/2; i+=2) {
1045. display.drawCircle(display.width()/2, display.height()/2, i, SSD1306_WHITE);
1046. display.display();
1047. delay(1);
1048. }
1050. delay(2000);
1051. }
1053. void testfillcircle(void) {
1054. display.clearDisplay();
1056. for(int16_t i=max(display.width(),display.height())/2; i>0; i-=3) {
1057. // The INVERSE color is used so circles alternate white/black
1058. display.fillCircle(display.width() / 2, display.height() / 2, i, SSD1306_INVERSE);
1059. display.display(); // Update screen with each newly-drawn circle
1060. delay(1);
1061. }
1063. delay(2000);
1064. }
1066. void testdrawroundrect(void) {
1067. display.clearDisplay();
1069. for(int16_t i=0; i<display.height()/2-2; i+=2) {
1070. display.drawRoundRect(i, i, display.width()-2*i, display.height()-2*i,
1071. display.height()/4, SSD1306_WHITE);
1072. display.display();
1073. delay(1);
1074. }
1076. delay(2000);
1077. }
1079. void testfillroundrect(void) {
1080. display.clearDisplay();
1082. for(int16_t i=0; i<display.height()/2-2; i+=2) {
1083. // The INVERSE color is used so round-rects alternate white/black
1084. display.fillRoundRect(i, i, display.width()-2*i, display.height()-2*i,
1085. display.height()/4, SSD1306_INVERSE);
1086. display.display();
1087. delay(1);
1088. }
1090. delay(2000);
1091. }
1093. void testdrawtriangle(void) {
1094. display.clearDisplay();
1096. for(int16_t i=0; i<max(display.width(),display.height())/2; i+=5) {
1097. display.drawTriangle(
1098. display.width()/2 , display.height()/2-i,
1099. display.width()/2-i, display.height()/2+i,
1100. display.width()/2+i, display.height()/2+i, SSD1306_WHITE);
1101. display.display();
1102. delay(1);
1103. }
1105. delay(2000);
1106. }
1108. void testfilltriangle(void) {
1109. display.clearDisplay();
1111. for(int16_t i=max(display.width(),display.height())/2; i>0; i-=5) {
1112. // The INVERSE color is used so triangles alternate white/black
1113. display.fillTriangle(
1114. display.width()/2 , display.height()/2-i,
1115. display.width()/2-i, display.height()/2+i,
1116. display.width()/2+i, display.height()/2+i, SSD1306_INVERSE);
1117. display.display();
1118. delay(1);
1119. }
1121. delay(2000);
1122. }
1124. void testdrawchar(void) {
1125. display.clearDisplay();
1127. display.setTextSize(1); // Normal 1:1 pixel scale
1128. display.setTextColor(SSD1306_WHITE); // Draw white text
1129. display.setCursor(0, 0); // Start at top-left corner
1130. display.cp437(true); // Use full 256 char 'Code Page 437' font
1132. // Not all the characters will fit on the display. This is normal.
1133. // Library will draw what it can and the rest will be clipped.
1134. for(int16_t i=0; i<256; i++) {
1135. if(i == '\n') display.write(' ');
1136. else display.write(i);
1137. }
1139. display.display();
1140. delay(2000);
1141. }
1143. void testdrawstyles(void) {
1144. display.clearDisplay();
1146. display.setTextSize(1); // Normal 1:1 pixel scale
1147. display.setTextColor(SSD1306_WHITE); // Draw white text
1148. display.setCursor(0,0); // Start at top-left corner
1149. display.println(F("Hello, world!"));
1151. display.setTextColor(SSD1306_BLACK, SSD1306_WHITE); // Draw 'inverse' text
1152. display.println(3.141592);
1154. display.setTextSize(2); // Draw 2X-scale text
1155. display.setTextColor(SSD1306_WHITE);
1156. display.print(F("0x")); display.println(0xDEADBEEF, HEX);
1158. display.display();
1159. delay(2000);
1160. }
1162. void testscrolltext(void) {
1163. display.clearDisplay();
1165. display.setTextSize(2); // Draw 2X-scale text
1166. display.setTextColor(SSD1306_WHITE);
1167. display.setCursor(10, 0);
1168. display.println(F("scroll"));
1169. display.display(); // Show initial text
1170. delay(100);
1172. // Scroll in various directions, pausing in-between:
1173. display.startscrollright(0x00, 0x0F);
1174. delay(2000);
1175. display.stopscroll();
1176. delay(1000);
1177. display.startscrollleft(0x00, 0x0F);
1178. delay(2000);
1179. display.stopscroll();
1180. delay(1000);
1181. display.startscrolldiagright(0x00, 0x07);
1182. delay(2000);
1183. display.startscrolldiagleft(0x00, 0x07);
1184. delay(2000);
1185. display.stopscroll();
1186. delay(1000);
1187. }
1189. void testdrawbitmap(void) {
1190. display.clearDisplay();
1192. display.drawBitmap(
1193. (display.width() - LOGO_WIDTH ) / 2,
1194. (display.height() - LOGO_HEIGHT) / 2,
1195. logo_bmp, LOGO_WIDTH, LOGO_HEIGHT, 1);
1196. display.display();
1197. delay(1000);
1198. }
1200. #define XPOS 0 // Indexes into the 'icons' array in function below
1201. #define YPOS 1
1202. #define DELTAY 2
1204. void testanimate(const uint8_t *bitmap, uint8_t w, uint8_t h) {
1205. int8_t f, icons[NUMFLAKES][3];
1207. // Initialize 'snowflake' positions
1208. for(f=0; f< NUMFLAKES; f++) {
1209. icons[f][XPOS] = random(1 - LOGO_WIDTH, display.width());
1210. icons[f][YPOS] = -LOGO_HEIGHT;
1211. icons[f][DELTAY] = random(1, 6);
1212. Serial.print(F("x: "));
1213. Serial.print(icons[f][XPOS], DEC);
1214. Serial.print(F(" y: "));
1215. Serial.print(icons[f][YPOS], DEC);
1216. Serial.print(F(" dy: "));
1217. Serial.println(icons[f][DELTAY], DEC);
1218. }
1220. for(int i=1;i<3;i++) { // changed to loop 2 times from Loop forever...
1221. display.clearDisplay(); // Clear the display buffer
1223. // Draw each snowflake:
1224. for(f=0; f< NUMFLAKES; f++) {
1225. display.drawBitmap(icons[f][XPOS], icons[f][YPOS], bitmap, w, h, SSD1306_WHITE);
1226. }
1228. display.display(); // Show the display buffer on the screen
1229. delay(200); // Pause for 1/10 second
1231. // Then update coordinates of each flake...
1232. for(f=0; f< NUMFLAKES; f++) {
1233. icons[f][YPOS] += icons[f][DELTAY];
1234. // If snowflake is off the bottom of the screen...
1235. if (icons[f][YPOS] >= display.height()) {
1236. // Reinitialize to a random position, just off the top
1237. icons[f][XPOS] = random(1 - LOGO_WIDTH, display.width());
1238. icons[f][YPOS] = -LOGO_HEIGHT;
1239. icons[f][DELTAY] = random(1, 6);
1240. }
1241. }
1242. }
1243. }